## Slide 1
ANALOG & ALL OPTICAL PROCESSORS
Transcription of Universal Digital Machines to Analog Computers
Two alternative architectures
Oscillator Networks – Sequential Optical Automata
Theophanes E. Raptis
rtheo@dat.demokritos.gr
Division of Applied Technologies
NCSR “Demokritos”

## Slide 2: Existing Paradigms Of Universal Computation
1. Claude Shannon’s GPAC : General Purpose Analog Computer (1945)
Not directly programmable w/out self-reconfigurable circuitry and digital interface
Cost vs accuracy exponentially increasing
2. Alan Turing’s UTM (Universal Turing Machine) + Churche’s λ-Calculus
Fully programmable
Von Neumann implementation – Digital Design – Boolean Circuits – Controllable accuracy.

## Slide 3: Limits of Conventional Computing
Memory – Speed Bottleneck.
Moore’s Law breakdown expected near 2025.
Heat generation increasing with dense transistor packing.
Landauer’s Principle: Entropy Increase/Logical gating ~ KT log(2).
Attempts for “Cold Computing”: Reversible Gates (Fredkin – Toffoli – Margolus 80s – Prequel to QGates).
Bennet: main source of actual entropy due to Memory Erasure during Read/Write operations.

## Slide 4: New Analog Optical Processing
Advantages:
1. Direct Transcription of UTM or other Discrete Automaton Protocol into Global Map of equivalent Dynamical System.
2. Optical Registers in alphabets higher than Binary! Great Information Compression – Denser Packing (W/Velengths/Optical Fiber).
3. No Digital Design/Boolean Logic at all -> No Need for Transistors/Gates!

## Slide 5: Simple UTM-Automaton Logic
Ordinary Discrete Automata defined by L = k+m+2 bits where k: memory states read, m: internal control states, 1 L/R motion, 1 R/W bit
Total Combinatory Space for Global Map:
Total States: 2^L+1 (0  Blank Memory)
Equivalence of Alphabet to Phase: k Complex Roots of Unity.
Equivalence of Current Machine State: 2^L+1 Reference Wavelengths.
Global Map: Transitions to Phase Shifts

## Slide 6: Example: k=3,m=2 (Simplest Wolfram’s UTM)
Input – Output Pairs formed by concatenation of memory + ctrl + motion bits
Phase modulation extracted by Output De-concatenation at prescribed length (A/D conversion)

## Slide 7: Correspondences

## Slide 8: Equivalent Optical Architecture-I

## Slide 9: Εquivalent Optical Architecture-II
“Cellular Automaton” equivalent through “individualization”.
Replacement of Ref. Wavelength w. single composite signal
Pass through Cyclic Permutation Gate
Extract 1st coefficient
Apply to each phase-ctrl-oscillator

## Slide 10: Block Correspondence

## Slide 11: Other Options Currently Available
Spectrum Encoding.
Take a single “beat” to represent a set of alphabet symbols over a carrier frequency.
Superposition of beats represents bytes. Possibility for higher alphabets (Hex).
Similar to “Shift-Key” modulation.
http://en.wikipedia.org/wiki/Multiple_frequency-shift_keying
Single Carrier possible w. OFDM / OAM Control.

## Slide 12
Difference from transmission systems: signals are to be Processed not Detected.
Advantage: whole register in a single signal
Ideally an infinite spectrum would contain a whole hard disk!
Possibility of “Collective Registers”. Analog of QC
Combinatory Set of all bytes present at beginning of computation. Difference only in the processing mode (parallel vs serial).
Classical analogues of Q. C. shown already in the language of Geometric Algebra by Aerts. [D. Aerts, M. Czahor et al, J. Phys. A: Math. Theor. 40(31), 2007, p. F753 ] (quant-ph/0611279)

## Slide 13: Transcription Protocols
Transcription of Heap/Stack machines into Tape Automata.
Extraction of Global Maps from resulting Automata.
Appropriate Turing Universal Automata:
SMETANA  SMITH
28 States C.A. Braktif (ALPACA Simulator, https://github.com/catseye/ALPACA)
https://esolangs.org/wiki/C2BF
Universal Bit-Bit-Jump Language [Mazonka http://arxiv.org/abs/0907.2173]
Subleq URISC architecture [Mazonka, Kolodin http://arxiv.org/abs/1106.2593]